## Slide 1
SMART BANK LOCKER SECURITY SYSTEM
Dual ESP32 Architecture for Encrypted PIN Transfer & Wireless Locker Authentication
IIT Jammu Summer School 2026
IoT & Embedded Systems • Hardware Security Mini-Project
Presented by Tannu & Mukul Bindal

## Slide 2
Why This Project?
Rethinking how a locker decides who to trust
Physical keypad locks can be tampered or shoulder-surfed.
Sending a PIN wirelessly in plain text invites sniffing attacks.
A single board has no separation between input and verification.
Wrong attempts often go unnoticed — no alarm, no warning.
The Core Idea
Split the locker's brain into two ESP32 nodes — one reads the PIN and encrypts it, the other verifies it and controls the lock. Neither node alone can be tricked into opening the locker.
Capture
→
Encrypt
→
Transmit
→
Decrypt & Verify
→
Actuate
Smart Bank Locker Security System | ESP32 Dual-Node Encrypted Access
2

## Slide 3
System Architecture
Master node reads and encrypts; slave node verifies and actuates
Keypad
Input
ESP32 - A (Master)
Reads PIN, encrypts with shared key, sends ciphertext
Wi-Fi /
Bluetooth
→
→
→
ESP32 - B (Slave)
Decrypts ciphertext, verifies PIN, drives outputs
→
Servo, LED
& Buzzer
Key Design Principle
The raw PIN never leaves ESP32 - A. Only encrypted data travels over the wireless link, so intercepting the transmission alone cannot reveal the PIN.
Wireless Link Choice
Wi-Fi (ESP-NOW): peer-to-peer, no router, very low latency — recommended
Bluetooth Classic / BLE: simple pairing, good short-range fallback
Smart Bank Locker Security System | ESP32 Dual-Node Encrypted Access
3

## Slide 4
Hardware Components
A minimal, low-cost bill of materials for the simulation
2 x ESP32 Dev Boards
One master (input side), one slave (locker side).
4x4 Matrix Keypad
For entering the numeric PIN on the master node.
Micro Servo Motor (SG90)
Simulates the physical locker bolt / latch.
Green & Red LEDs
Visual status for access granted / denied.
Piezo Buzzer
Audible alarm triggered on wrong PIN attempts.
Breadboard & Jumper Wires
For prototyping both ESP32 nodes on Wokwi / hardware.
Smart Bank Locker Security System | ESP32 Dual-Node Encrypted Access
4

## Slide 5
Encryption & Decryption Logic
A shared secret key turns the PIN into unreadable data before it is sent
PIN
(1234)
→
Encrypt
(XOR / AES key)
→
Ciphertext
(sent over link)
→
Decrypt
(same key)
→
Compare
& Verify
On ESP32 - A (Master)
Entered PIN is combined with a pre-shared secret key using a lightweight cipher (XOR, or AES-128 for stronger security)
Only the resulting ciphertext is placed on the Wi-Fi / Bluetooth packet — never the raw PIN
On ESP32 - B (Slave)
Receives ciphertext and decrypts it using the identical shared key stored in its firmware
Decrypted PIN is compared with the reference PIN to decide access — match or mismatch
Smart Bank Locker Security System | ESP32 Dual-Node Encrypted Access
5

## Slide 6
Working Flow & Security Features
What ESP32 - B does once the PIN is verified, plus what keeps the system tamper-resistant
PIN Matches
Servo unlocks the bolt; green LED turns ON
Optional confirmation tone on the buzzer
Locker auto-relocks after a set delay
PIN Mismatches
Bolt stays engaged; red LED turns ON / blinks
Buzzer sounds an alarm to alert nearby staff
Repeated failures trigger a temporary lockout
Additional Security Layers
Encrypted Transmission
Only ciphertext travels wirelessly
Split Trust Model
Input & verification on separate nodes
Attempt Lockout
Pauses system after repeated failures
Shared-Key Design
Only boards with the key can decrypt
Smart Bank Locker Security System | ESP32 Dual-Node Encrypted Access
6

## Slide 7
Applications & Future Scope
Where It Applies
Bank lockers and vault access points
Office server-room or cabinet security
Smart-home safes and storage boxes
What's Next
Upgrade cipher from XOR demo to full AES-128 / 256
Add fingerprint or RFID as a second factor
Log attempts to the cloud and control via a mobile app
Thank You